## Slide 1: FPGA-LAB Overview

## Slide 2: FPGA - Field Programmable Gate Array
Logical Element
Programmable Routing

## Slide 3: FPGA market target
Unit cost
per performance
at production
Initial development and manufacturing Cost
NRE - Non-recurring engineering
Custom
Chip
ASIC
FPGA
Software
FPGA main use cases
Low Volumes
Prototyping
Emulation
Feature | FPGA | ASIC
Time to Market | Fast | Slow
NRE | Low | High
Design Flow | Simple | Complex
Unit Cost | High | Low
Performance | Low | High
Power consumption | High | Low
Unit Size | High | Low
FPGA VS ASIC

## Slide 4: Advance FPGA with embedded commonly used hard-macros

## Slide 5: Development Flow
Architecture
Design
Requirement
HDL Design
(Verilog etc.)
Test Environment
Behavioral
Simulation
Synthesis
Analysis
Bitstream

## Slide 6: Enics FPGA-Lab configuration
FPGA DEVICE
MY DESIGN INTERFACE WRAP
My Design
ACCESS REGISTERS
UART
ACCESS
8x32b input regs
8x32b output regs
My input ports
My output ports
Design specific
port assignment
rx
tx
REMOTE Terminal
/ Python Interface
USB-UART Cable